## Slide 1: Broadband Millimeter-Wave Antenna-on-Chip Development Richard Pierce, University of Texas at Dallas, GRC/TxACE
OBJECTIVE: Develop a broadband antenna for integration for on-chip solutions.
APPROACH: Utilize a broadband uniplanar antenna with EBG enhanced reflector in post processed thick film dielectric layers.
On-Chip Solution (> 100 GHz)
  Post Process Dielectrics (SU-8 or BCB)
  Modified Aperture Bowtie with EBG Reflector
  EBG Reflector Reduces Surface Waves and Isolates Antenna
  from High Loss Si
Measurements of SU-8 Material Properties Above 100 GHz
Develop Processes for Post Processed Thick Film Fabrication
RESULTS: Enables the integration of broadband high
performance antennas on top of a CMOS
substrate while maintaining high radiation efficiency and broadside gain.